## Slide 1: Environmental influence
Production influence
The first aspect concerning the environmental influence of the car is its production. Below are some ideas to reduce environmental impact of the car production:
Limitate the shavings
  By dividing one part into several (Upper bearing support, Uprights, …)
  By using alternative manufacturing processes (3D printing, …)
Recycle the shavings
Reducion of oil consumption
  Emulsion as lubricant (95% of water/5% water)
  Dry cutting
Purchase of second-hand part for the car (engine, …)
Reduce the number of scraps
  Cleaning of the machines
  Increase of metrology on the parts
Promote local production
Limitation of consumables
  Cleaning clothes
  Abrasive stones rather than sand paper
  Protective gloves reusable
Energy management
The recycling of the materials of the car is a very important aspect of the environmental influence of the vehicle production.
Some materials can be easily recycle (metallic materials for instance).
Some part bought on the market can be sold as second-hand.
Other materials are more difficult to recycle:
  Composite materials
  Tires
  Oils
Comparing to other teams, materials such as CFRP, … which can be difficult to recycle, are not widely used on our car.
However, even these materials can be recycled. Below, 2 examples are developed: recycling of tires and recycling of CFRP.
Materials recycling
Recycling of tires
Recycling of CFRP
Crush
Material/ Thermal recycling: Raw material or fuel for Cement and Blast furnace
Thermal recycling: Combustion
Separation
Fiber
Resin
Thermal/Chemical Recyling: Decomposed oil (fuel)
Material recycling: CFRP raw material
CFRP waste
Material recycling: Raw material of CFRP
Rubber powder/ aggregates
Grinding
Steel wires
Pyrolise, Grinding, …
Material recycling
Material recycling: Raw material
Material recycling
Fibers
Recycling
Crushing
Retreated tires
Material recycling
Magnetic/ Fiber separation